## Slide 1: Monolithic 3D – The Most Effective Path for Future IC Scaling
MonolithIC 3D Inc. Patents Pending
1

## Slide 2: Agenda:
Semiconductor Industry is reaching an inflection point
Monolithic 3D IC – The next generation technology driver
  Monolithic 3D – Game Change, using existing transistor process !
Heat removal
The MonolithIC 3D Advantages
Summary

## Slide 3: Martin van den Brink -EVP & CTO, ASML ISSCC 2013 & SemiconWest 2013

## Slide 4: The Current 2D-IC is Facing Escalating Challenges
On-chip interconnect is
  Dominating device power consumption, performance and cost
B. Wu, A. Kumar, Applied Materials

## Slide 5: 3D and EDA need to make up for Moore’s Law, says Qualcomm*
“Qualcomm is looking to monolithic 3D and smart circuit architectures to make up for the loss of traditional 2D process scaling as wafer costs for advanced nodes continue to increase. .. Now, although we are still scaling down it’s not cost-economic anymore”
“Interconnect RC is inching up as we go to deeper technology. That is a major problem because designs are becoming interconnect-dominated. Something has to be done about interconnect. What needs to be done is monolithic three-dimensional ICs.”
“TSV...are not really solving the interconnect issue I’m talking about.
So we are looking at true monolithic 3D. You have normal vias between different stacks.”
* Karim Arabi Qualcomm VP of engineering, DAC 2014 Key Note
<http://www.techdesignforums.com/blog/2014/06/05/karim-arabi-monolithic-3dic-dac-2014/>

## Slide 6: Monolithic 3D Qualcomm SoCs by 2016* *EE Times 3/31/2015 <http://www.eetimes.com/document.asp?doc_id=1326174&piddl_msgid=338050#msg_338050>
“3DV, enables die size to be shrunk in half, while simultaneously increasing yields,“
Qualcomm's motivation, according to Arabi, is market share in the 8 billion smartphones that he predicts will be produced from 2014 to 2018
In the fabrication process of front-to-back (F2B) 3DVs (a) the bottom tier is created the same way as 2D-ICs. (b,c,d) To add another layer, first a thin layer of silicon is deposited on top of the bottom tier. (e) This front-end-of-line (FEOL) process of the top tier permits the addition of normal vertical vias and top-tier contacts. (f) Finally back-end-of-line (BEOL) processing creates the top-tier. (Source:Qualcomm)

## Slide 7
Even Intel Agrees – 7nm is the Limit for Silicon ISSCC 2015

## Slide 10: Conclusions:
Dimensional Scaling (“Moore’s Law”) is already exhibiting diminishing returns
The road map beyond 2017 (7nm) is unclear
While the research community is working on many interesting new technologies (see below), none of them seem mature enough to replace silicon for 2019
    - Carbon nanotube - Indium gallium arsenide - 2D (MoS2, etc.) transistors
    - Graphene - Spintronics
    - Nanowire - Molecular computing
    - Photonics - Quantum computing
3D IC is considered, by all, as the near-term solution, Monolithic 3D IC is well positioned to be so, as it uses the existing infrastructure!
  It is safe to state that Monolithic 3D is the only alternative that could be ready for high volume in 2019 !!

## Slide 11
11
MONOLITHIC 10,000x the Vertical Connectivity of TSV

## Slide 12
12
Processing on top of copper interconnects should not make the copper interconnect exceed 400oC
    How to bring mono-crystallized silicon on top at less than 400oC
    How to fabricate state-of-the-art transistors on top of copper interconnect and keep the interconnect below at less than 400oC
Misalignment of pre-processed wafer to wafer bonding step used to be ~1µm
    How to achieve 100nm or better connection pitch
    How to fabricate thin enough layer for inter-layer vias of ~50nm
The Monolithic 3D Challenge
Why is it not already in wide use?

## Slide 13: MonolithIC 3D – Innovative Flows
RCAT (2009) – Process the high temperature on generic structures prior to ‘smart-cut’, and finish with cold processes – Etch & Depositions
Gate Replacement (2010) (=Gate Last, HKMG) - Process the high temperature on repeating structures prior to ‘smart-cut’, and finish with ‘gate replacement’, cold processes – Etch & Depositions
Laser Annealing (2012) – Use short laser pulse to locally heat and anneal the top layer while protecting the interconnection layers below from the top heat
Game Change, using existing transistor process !
Modified ELTRAN (2015) – Use ELTRAN for low cost, No defects, Existing transistor flow
Precise Bonder (2014) – Use new precise bonders, offering low cost flow with minimal R&D

## Slide 14: ELTRAN® - Epitaxial Layer TRANsfer
Originated, developed and produced at Canon Inc.
‘

## Slide 15: M3D Leveraging the ELTRAN Idea
Both donor and carrier wafer could be pre-processed
  Donor wafer:
  Carrier wafer:
No impact on processed layer or on device processing
Donor and Carrier could be easily recycled – reused
Minimal incremental cost per layer (porous + epi <$20)
porous ‘cut’ layer
epi. layer
Base wafer - reused
porous ‘cut’ layer
oxide layer
Base wafer - reused

## Slide 16
16
~700 µm Donor Wafer
Use standard flow to process “Stratum 3”
- using ELTRAN donor wafer (through silicidation)
MonolithIC 3D Inc. Patents Pending
Stratum 3
porous layer
PMOS
NMOS
Silicon
Poly
Oxide
STI
epi

## Slide 17
17
~700µm Donor Wafer
Silicon
Bond to a ELTRAN carrier-wafer
~700µm Carrier Wafer
STI
oxide to oxide bond
porous layer

## Slide 18
18
~700µm Donor Wafer
‘Cut’ Donor Wafer off
~700µm Carrier Wafer
Transferred ~100nm Layer
- Stratum 3
Silicon
Silicon
STI

## Slide 19
19
Etch Off the Porous Silicon and Smooth
~700µm
Carrier Wafer
~100nm
STI
Silicon
Oxide
porous layer

## Slide 20
20
Use standard flow to process “Stratum 2”
Note: High Temperature is OK
~100nm Layer
~700µm
Carrier Wafer
Silicon
Porous ‘cut’ layer
STI
High Performance Transistors
Oxide
Stratum 2
Stratum 3
Need to set
vertical isolation

## Slide 21
21
Add at least one interconnect layer
~700µm
Carrier Wafer
~100nm
Transferred Layer
Stratum-2 copper interconnection layers
Stratum 2
Stratum 3
For some applications such as
Image Sensor, this could be it !

## Slide 22
MonolithIC 3D Inc. Patents Pending
22
Transfer onto Final carrier
~700µm
Carrier Wafer
Oxide-oxide bond
Transferred
Layer (Stratum 2 +Stratum 3)
Final Carrier
porous ‘cut layer

## Slide 23
MonolithIC 3D Inc. Patents Pending
23
Remove carrier-wafer
Oxide-oxide bond
Transferred
Layer (Stratum 2 +Stratum 3)
Final Carrier

## Slide 24
MonolithIC 3D Inc. Patents Pending
24
Add Stratum-3 Interconnections
Oxide-oxide bond
Transferred
Layer (Stratum 2 +Stratum 3)
Final Carrier

## Slide 25: Precise Bonder – Multi-Strata M3D
Utilizing the existing front-end process !!!
  <200 nm (3σ)
Achieving 10,000x vertical connectivity as the upper strata will be thinner than 100 nm
  Mix – Sequential/Parallel M3D
  Low manufacturing costs

## Slide 27
MonolithIC 3D Inc. Patents Pending
27
Transfer onto Pre-Processed Wafer
~700µm
Carrier Wafer
Oxide-oxide bond
Transferred
Layer (Stratum 2 +Stratum 3)
Base Wafer
PMOS
NMOS

## Slide 28
MonolithIC 3D Inc. Patents Pending
28
Remove Carrier Wafer
Oxide-oxide bond
Transferred
Layer (Stratum 2 +Stratum 3)
Base Wafer
PMOS
NMOS

## Slide 29
MonolithIC 3D Inc. Patents Pending
29
Connect to Stratum 1
Oxide-oxide bond
Transferred
Layer (Stratum 2 +Stratum 3)
Base Wafer
PMOS
NMOS

## Slide 30
MonolithIC 3D Inc. Patents Pending
30
Add Metal Layers
Oxide-oxide bond
Transferred
Layer (Stratum 2 +Stratum 3)
Base Wafer
PMOS
NMOS

## Slide 31: Monolithic 3D using ELTRAN & Precise Bonder
Utilizes existing transistor process
Could help upgrade any fab (leading or trailing)
Very competitive cost structure
Better power, performance, price than a node of scaling at a fraction of the costs !!!
Allows functionality that could not be attained by 2D devices

## Slide 32: The Operational Thermal Challenge
Upper tier transistors are fully surrounded by oxide and have no thermal path to remove operational heat
Good Heat Conduction
~100 W/mK
Poor Heat Conduction
~1 W/mK

## Slide 33: The Solution
Use Power Delivery (Vdd, Vss) Network (“PDN”) also for heat removal
Add heat spreader to smooth out hot spots
Add thermally conducting yet electrically non-conducting contacts to problem areas such as transmission gates

## Slide 34: Cooling Three-Dimensional Integrated Circuits using Power Delivery Networks (PDNs)
Hai Wei, Tony Wu, Deepak Sekar*, Brian Cronquist*, Roger Fabian Pease, Subhasish Mitra
Stanford University, Monolithic 3D Inc.*
34
IEDM 2012 Paper

## Slide 35: Monolithic 3D Heat Removal Architecture (Achievable with Monolithic 3D vertical interconnect density)
Global power grid shared among multiple device layers, local power grid for each device layer
Local VDD grid architecture shown above
Optimize all cells in library to have low thermal resistance to VDD/VSS lines (local heat sink)
px
py
Patented and Patent Pending Technology
Without Power Grid
With Power Grid
Signal wire
Heat sink

## Slide 36
  1. Reduction die size and power – doubling transistor count - Extending Moore’s law
  Monolithic 3D is far more than just an alternative to 0.7x scaling !!!
  2. Significant advantages from using the same fab, design tools
  3. Heterogeneous Integration
  4. Multiple layers Processed Simultaneously - Huge cost reduction (Nx)
  Logic redundancy => 100x integration made possible
  3D FPGA prototype, 2D volume
  7. Enables Modular Design
  8. Naturally upper layers are SOI
  9. Local Interconnect above and below transistor layer
  10. Re-Buffering global interconnect by upper strata
  11. Others
  A. Image sensor with pixel electronics
  B. Micro-display
The Monolithic 3D Advantage

## Slide 37: Summary
We have reached an inflection point
Multiple practical paths to monolithic 3D exist
Heat removal of monolithic 3D could be designed in
Breaking News – The process barriers are now removed
=> Monolithic 3D – The Most Effective Path for Future IC Scaling